Nema-zag circuit simulator 2000 😎

Technical document

# Introduction
The purpose of this document is to document the design principles of the Nema-zag circuit simulator 2000 😎 and to illustrate the different simulation types, and how to use them.
The Nema-zag circuit simulator 2000 😎 is a circuit simulator capable of solving linear circuits in steady state (non-linear and transient analysis planned).
It’s composed of two main modules, the simulation engine, and the GUI. The simulation engine is the part that does the actual simulation, it takes a netlist, and a simulation type, and performs the simulation. On the other hand, the GUI is responsible for providing the user with a tool to edit schematics graphically, as well as select the simulation type. It also is responsible for displaying the results out for the user, and building sub-circuits.
# I – The Simulation Engine
The simulation engine is an analog circuit simulator that solves circuits using MNA (Modified Nodal Analysis). Different types of simulation can be done, including DC, AC, sweep…
Here, we look into different aspects of the simulation engine with more detail.

## Netlist Format
The netlist format is quite similar to the traditional SPICE format, it’s as follows for components:
ComponentType ComponentIdentifier Node1 Node2... Value1 Value2…
- The spacer is the space.
- New lines separate different components or commands.
- ComponentType denotes the type of the component as shown in the table below.
- ComponentIdentifier is the unique name given to a component in order to aid in sweep analysis and identifying currents.
- Node1, Node2… are all the nodes the component is connected to, separated by a space, different components connect to different numbers of nodes.
- Value1, Value2… are all the values a component takes, like the voltage, frequency and phase of a voltage source.
Name	Type	# of nodes	Value 1	Value 2	Value 3
Resistor	R	2	Resistance	-	-
Conductor	G	2	Conductance	-	-
Inductor	L	2	Inductance	-	-
Capacitor	C	2	Capacitance	-	-
Voltage Source	V	2	Max. Voltage	Frequency	Phase
Current Source	I	2	Max. Current	Frequency	Phase
Operational Amplifier	OPAMP3	3	-	-	-
Differential Amplifier	DIFFAMP3	3	Gain	-	-

## Command Format
As of now, the engine supports the following simulation types.
- DC Operating Point
- DC Parameter Sweep
- AC Operating Point
- AC Parameter Sweep